## Slide 1
By Vicky Huang and Daniel Bedoya
Method comparison of monitoring COVID-19 virus through wastewater-based epidemiology

## Slide 2: Team
Dr. Ian Bradley
Dr. Yinyin Ye
Vicky Huang
Danya Hanin
Sydney Gallo
Daniel Bedoya
Joyce Wang
Emily Segelhurst
UG
MS

## Slide 3
Wastewater-based epidemiology analyzes wastewater to determine the consumption of, or exposure to, chemicals or pathogens in a population.
Wastewater Based Epidemiology (WBE)
Early detection & mitigation window
SARS-CoV-2 in feces as soon as...
3 days after infection
5 days before symptoms
7 days before hospitalization
Notes: Add information of the

## Slide 4: NYSDOH state-wide surveillance network

## Slide 5: Western New York Watersheds
*MGD: million gallons per day
Sewershed​ | Permit Flow Rate (MGD)​ | Population​
City of Tonawanda​ | 2.5-5​ | 14,873​
Lackawanna​ | 4.5​ | 17,859​
Southtowns​ | 16​ | 94,616​
Kenmore Tonawanda​ | 25​ | 70,470​
Amherst​ | 48​ | 140,324​
Bird Island​ | 180​ | 437,357​

## Slide 6: Overview of 6 methods
Tangential-flow ultrafiltration
Solids
Polyethylene glycol (PEG) precipitation
Ultracentrifugation
Electronegative membrane filtration
Nanotrap magnetic beads

## Slide 7: PCR Detection
Amplification
Genome Sequencing
Gene Detection
MATCH:

## Slide 8
Challenges of detection
Wastewater
Concentration
Purification
SARS-CoV-2 genes in wastewater are in low concentration
Wastewater contains non-viral substances that may inhibit downstream detection
PCR inhibitors: urea, blood, body fluids, water, soil, etc.
Notes: Add explanation for PCR inhibitors:
PCR method is prone to inhibiting substances that may present in the samples. Which can affect the sensitivity of detection or even lead to bad result. It’s important to remove the potential inhibitors. Some of the common inhibitors in wastewater are urea, blood, body fluids, water, soil

## Slide 10: Tangential-flow ultrafiltration (UF)
Stage3
Ultracentrifuge
250 ml
Notes: *625 times concentrated
Talk about why we are concentrating the ML

## Slide 11: Goals
Comparison of virus detection sensitivity
Comparison of costs
Comparison of scalability

## Slide 12: Task 1: Assess the PCR inhibition removal from wastewater concentrated by commercial nucleic acid extraction kits
Hypothesis: Commercial extraction kits cannot effectively remove PCR inhibition.
QIAGEN QIAamp
DSP Virus Kit
ZYMO Quick
DNA/RNA Viral Kit
Nucleic acid extraction
6 sewersheds
RT-qPCR
undiluted
1 x
5-fold dilution
5 x
10-fold dilution
10 x
Virus concentration
250 mL
100 mL
Ultrafiltration
PEG
Spike in BCoV at 7×108 gene copies
Notes: PCR inhibitors are any factor which inhibit the detection in PCR later on in the experiment.
BCoV gene copies detected by RT-qPCR (qPCR stands for quantitative polymerase chain reaction and is a technology used for measuring DNA using PCR.)
Deliverable: compare recovery of BCov genes by different nucleic acid extraction kits and determine the dilution factor that is needed for qPCR analysis

## Slide 13
Result: BCoV (gene copies/µL PCR reaction)
1x, 5x and 10 x dilution prior to PCR
Notes: Interpretations on the result:
10x dilution is selected for task 2 based on the result of task 1. Highest BCoV gene copies shown from both kits for all the methods

## Slide 14
Task 2. Compare the extraction efficiencies of exogenous and endogenous viral nucleic acids from wastewater concentrates​
14
QIAGEN QIAamp
DSP virus Kit
ZYMO Quick
DNA/RNA Viral Kit
QIAGEN RNeasy
PowerMicrobiome Kit
ZYMO Quick RNA
Bacterial/Fungal Microprep
Nucleic acid extraction
Bead beating
4000 rpm
1 min
or 5 min
RT-qPCR
10-fold dilution
BCoV
PMMoV
CrAssphage
SARS-CoV-2
BCoV
4×107 gene copies/mL
Virus concentration
250 mL
100 mL
Ultrafiltration
PEG
3 L
Pooled
500 mL
6 sewersheds
Notes: Goal: To make a decision for kits
Two key points:
Compare exogenous and endogenous viral nucleic acids at the same initial levels; pooling samples
Pool samples are used from combining water samples from 6 sewer sheds because we focus on the efficiency of extraction here, not the recovery of genes from each location

## Slide 15
Result: Commercial extraction kits recovered exogeneous and endogenous viral nucleic acids with varying efficiency rates.
​
QIAGEN
ZYMO
Notes: know the full names of each virus
Ultrafiltration: zymo shows better with higher detection on 3 viruses
PEG: zymo shows slightly better with less sparity

## Slide 16
UF Cost analysis and scalability
Challenges : manual labor and training; high investment
Reusable period for non-recurring cost: 1year
Total cost: $5594 (maximized 6 samples per run)
Item | Quantity | Unit Price | Total
VWR PIPETTE SERO 50ML PR CS100 | 6 | 0.89 | 5.37
MilliporeSigma™ Sucrose, OmniPur™, Calbiochem™ 8510-500GM(ml) | 30 | 0.07 | 1.96
Sorensen microcentrifuge tubes 2ML PK400 | 6 | 0.06 | 0.36
Sodium Hydroxide (Pellets/Certified ACS), Fisher Chemical™ (g) | 40 | 0.06 | 2.25
Gibco PBS, pH 7.4 (ml) | 1.2 | 0.03 | 0.03
PYREX™ Reusable Glass Serological Pipets, TD, Color-Coded | 1 | 9.66 | 9.66
VWR® Disposable Pasteur Pipets, Flint Glass | 6 | 0.20 | 1.22
VWR universal tips, filtered, sterile, standard, 100-1250 ul | 6 | 0.03 | 0.18
Total Cost Per Run |  | 10.99 | 21.02
Recurring Costs
Item | Quantity | Unit Price | Total
Vivaflow 50R Hydrostart membrane 30 kDa, VF05H2 | 6 | 216.81 | 1300.86
Sartorius Vivaflow™ Models Accessories: Diafiltration Reservoir | 6 | 187.64 | 1125.84
VWR® Media/Storage Bottles with GL Screw Caps | 2 | 6.74 | 13.49
NaOH waste collection bottle | 1 | 33.12 | 33.12
Polypropylene 250 ml centrifuge bottles | 6 | 11.87 | 71.25
Ultracentrifuge tube | 6 | 4.78 | 28.68
sartorius vuvaflow 50R | 2 | 1500 | 3000
Total Cost |  | 1960.97 | 5573.24
Non-Recurring Costs
Notes: Recurring total cost for 6 samples is $21; non-recurring cost is $5,500 including …..but sustained for up to an year with proper maintanence
Challenges: manual labor and training for stage in ultrafiltration
Specific 6 samples per run

## Slide 17
PEG Cost analysis and scalability
Item | Quantity | Unit Price | Total
Polyethylene glycol (PEG) 8000 | 48 g | 0.08 | 3.70
VWR Serological Pipettes | 6 tips | 0.89 | 5.37
Sorenson Microcentrifuge tubes | 7 tubes | 0.03 | 0.23
Gibco Phosphate Buffered Saline (PBS) | 1.2 mL | 0.02 | 0.03
VWR filtered pipette tips | 6 tips | 0.05 | 0.33
Sodium Chloride (NaCl) | 17.4 g | 0.03 | 0.53
 |  | Total Cost per Run: | 10.19
Recurring Costs
Item | Quantity | Unit Price | Total
250 ml Polypropylene Centrifuge Bottles | 12 | 11.88 | 142.56
 |  | Total Cost: | 142.56
Non-Recurring Costs
Challenges: time consuming
Advantages: Cheap cost & high potential to scale up
Total cost: $152.75 (maximized 6 samples per run)
Notes: Advantages: much cheaper compared to UF with very low initial cost(no equipment needed); high potential to scale up
Challenge: time consuming-up to 6 hours; but no need to watch in incubator
Total cost around $150

## Slide 18: Future work and expected deliverables
Compare to other methods (UG, S, EMF, KF)
Investigate the effects of wastewater analysis workflows on the downstream virus detection
  PCR detection
  genome sequencing
Notes: Future work: sequencing for variance and compare to other methods

## Slide 19
Ultrafiltration
PEG
Do these virus concentration methods work equally well for genome sequencing?
Ultrafiltration had the higher recoveries of viruses from wastewater.
Notes: UF works better from the data so far, showing more gene copies from the detection; downside back to high cost and labor demand
Next question is along with the future work, do this result work equally well for genome sequencing? Will there be a superior method?