## Slide 1: Revised Part 360 Series Solid Waste Management Facility Regulations
Air & Waste Management Association – Niagara Frontier Section
Annual Enrichment Seminar
Buffalo, NY
January 3, 2018
Richard Clarkson
Division of Materials Management
NYSDEC

## Slide 2: Background
First major revision in nearly 25 years
The Part 360 series rulemaking process formally began in February 2016
Conducted extensive public outreach that included two public comment periods, five public hearings, and more than 25 workshops and technical meetings with stakeholders
Reviewed and provided responses to thousands of comments.
The Regulations were published in the State Register and ENB and posted on DEC website on 9/20/17
Regulations became effective on 11/4/17

## Slide 3: Part 360 Revised Series Structure
Part 360 General Requirements
Part 361 Material Recovery Facilities
Part 362 Combustion, Thermal Treatment, Transfer, and Collection Facilities
Part 363 Landfills
Part 364 Waste Transporters
Part 365 Regulated Medical Waste and Other Infectious Wastes
Part 366 Local Solid Waste Management Planning
Part 369 State Assistance Projects

## Slide 4: Part 360
Solid Waste Management Facilities
General Requirements

## Slide 5: Part 360 – SWMF Program Structure
Exempt Facilities
    Established in regulation
    No additional approval from DEC
Registered Facilities
    Facility types established in regulation
    Operating requirements established in regulation
    Ministerial Action: no SEQR or UPA
Permitted Facilities
    Permit application reviewed by DEC
    Facility-specific special conditions can be applied
    SEQR and UPA apply

## Slide 6: Section 360.4
Transition

## Slide 7: 360.4 – Transition Requirements
Default: New regulations apply May 3, 2018
Existing registered facilities:
180 days to apply for a new registration, except for CDDHRFs which have 545 days
Existing permitted facilities:
        Permit in effect continues until renewal or modification
Existing exempt/registered facility now requiring permit:
Must have a complete application on file with the Department within 365 days, except for CDDHRFs which have 545 days

## Slide 8: 360.4 – Transition Requirements - Exempt Facility, Transporter or Collection Event
Exempt Registration
Must comply with registration notification within 180 days
Must remain in compliance with the requirements of the exemption until the new registration is validated by the Department
Exempt Permit
Must have a complete application on file with the Department within 365 days

## Slide 9: 360.4 – Transition Requirements - Retrofitting
Retrofitting of existing facilities that were exempt, registered, or permitted is not required
New structural components built after November 4, 2017 must comply with new requirements

## Slide 10: Section 360.12
Beneficial Use

## Slide 11: Part 360 Transition Requirements - BUDs
Pre-determined BUDs
    Expire May 3, 2018 if no longer included in section 360.12
    May be eligible for a case-specific BUD
Case-specific BUDs
    Expire on May 3, 2018 unless a renewal request is submitted by that date
    Exception – BUDS with specific expiration dates

## Slide 12: 360.12 – Beneficial Use
Subdivisions:
  (a) Applicability
  (b) Unacceptable Uses
  (c) Pre-determined Beneficial Uses (28)
  (d) Case-specific beneficial use determinations – general
  (e) Case-specific BUDs – navigational dredged material
  (f) Case-specific BUDs – gas storage brine or production brine

## Slide 13: 360.12(d) – Case-Specific Beneficial Use Determinations - General
Review criteria (“essential nature is use not disposal,” “managed as a commodity,” “will not adversely affect health and the environment,” etc.)
Lower of 6 NYCRR 375-6.8(b) Protection of Public Health and Protection of Groundwater Soil Cleanup Objectives for soil-like materials placed on the land
All case-specific BUDs expire no more than 5 years from effective date
Annual reporting for all case-specific BUDs
Right to hearing for revocation

## Slide 14: Section 360.13
Special Requirements for Pre-Determined Beneficial Use of Fill Material

## Slide 15: 360.13(a) – Applicability
Section 360.13 allows for the self-assessment of fill materials for appropriate use within 360.13 criteria
Section 360.13 DOES NOT:
Require sampling of material sent to CDDHRFs
Require all excavated soil or fill to be sampled
Prevent anyone from petitioning for a case-specific BUD pursuant to 360.12(d) for fill material

## Slide 16: 360.13(c) – Exemption of On-Site Reuse of Fill Material
Materials excavated at a site can be used anywhere on the site in areas of similar physical characteristics
If contaminated material will be used on a site with public access, minimum of 1 foot of clean soil cover must be placed
Not applicable to Part 375 program sites

## Slide 17: 360.13(f) – Acceptable Fill Material Uses
Fill Material Type | Fill Material End Use | Physical Criteria | Maximum Concentration Levels
General Fill | Any setting where the fill material meets the engineering criteria, for use, except: Undeveloped land; and Agricultural crop land. | Only soil, sand, gravel or rock; no non-soil constituents. | Lower of Protection of Public Health-Residential Land Use and Protection of Groundwater in Table 375-6.8(b) of this Title.

## Slide 18: 360.13(f) – Acceptable Fill Material Uses
Fill Material Type | Fill Material End Use | Physical Criteria | Maximum Concentration Levels
Restricted-Use Fill | For embankments or subgrade in transportation corridors, or on sites where in-situ materials exceed Restricted-Use Fill or Limited-Use Fill criteria. Must be placed above the seasonal high water table. | Up to 40 percent by volume inert, non-putrescible non-soil constituents. | General Fill criteria except that up to 3 mg/kg total benzo (a)pyrene (BAP) equivalent. No detectable asbestos.

## Slide 19: 360.13(f) – Acceptable Fill Material Uses
Fill Material Type | Fill Material End Use | Physical Criteria | Maximum Concentration Levels
Limited-Use Fill | Under foundations and pavements above the seasonal high water table | No volume limit for inert, non-putrescible non-soil constituents. | General Fill criteria, except up to Protection of Public Health-Commercial SCOs for metals; up to 3 mg/kg benzo(a)pyrene equivalent is allowed. No detectable asbestos.

## Slide 20: Section 360.14
Exempt Facilities

## Slide 21: 360.14 – Exempt Facilities
Management of waste (other than disposal) at site of generation or other location in the state under the same ownership or control as the site of waste generation
    Applicable across municipal agencies
    Not available for 7 specific facilities (slaughterhouse waste composting, deconstructing manufactured homes, surface impoundments for coal ash, others)
Non-putrescible waste storage on vehicle ≤ 10 days (with conditions)
Rendering facility
Facility storing less than 1000 waste tires
Pharmaceutical waste collection (with conditions)

## Slide 22: Section 360.15
Registered Facilities, Transporters and Collection Events

## Slide 23: 360.15 - Registered Facilities, Transporters and Collection Events
Certain Facilities are eligible for registration instead of permitting
Registrations are ministerial actions
Required to submit a registration form and declare the intended storage volumes and maximum throughput limits
Registrations valid for 5 years (except for waste transporters and HHW collection events)
Two or more registrations at the same site may require a permit if potential to cause significant adverse impacts exist
Registered activity at a permitted facility may be required to be included facility’s permit
Department may require financial assurance

## Slide 24: Section 360.22
Financial Assurance

## Slide 25: 360.22 – Financial Assurance
Acceptable mechanism: Trust Fund, Surety Bond Guaranteeing Payment, Letter of Credit, Local Gov’t Financial Test, Local Gov’t Guarantee
Standby Trust Fund only required for Bonds or LOCs ≥ $50,000
Specific facilities required to provide financial assurance, and DEC has authority to require it of any registered or permitted facility
Post-closure care and Custodial case cost estimates must be based on a rolling 30-year periods
Initial custodial care cost estimate must be submitted as part of the custodial case demonstration

## Slide 26: 360.22 – Financial Assurance
Transfer of fully funded post-closure mechanism from private landfill operator to municipal landfill owner upon closure or end of operator responsibility
Allowance for reducing financial assurance required by DEC by the amount of financial assurance required for the same facility by another municipality
Specific wording for trust funds, surety bonds, LOCs now included in regulation
Contingency factor – staggered as cost estimate increased
    15% for < $1 million, 10% for $100,000 - $1 million, 5% for > $1 million

## Slide 27: Part 361
Material Recovery Facilities

## Slide 28: Part 361 Material Recovery Facilities
Subpart 361-1 Recyclables Handling and Recovery Facilities
Subpart 361-2 Land Application and Associated Storage Facilities
Subpart 361-3 Composting and Other Organics Processing Facilities
Subpart 361-4 Mulch Processing Facilities
Subpart 361-5 Construction and Demolition Debris Handling and Recovery Facilities
Subpart 361-6 Waste Tire Handling and Recovery Facilities
Subpart 361-7 Metal Processing and Vehicle Dismantling Facilities
Subpart 361-8 Used Cooking Oil and Yellow Grease Processing Facilities
Subpart 361-9 Navigational Dredge Material Handling and Recovery Facilities

## Slide 29: Subpart 361-1
Recyclables Handling and Recovery Facilities

## Slide 30: 361-1 – Recyclables Handling and Recovery Facilities – Exempt & Registered Facilities
Exempt Facilities
Take-back sites operated by retailers or wholesalers for their products or similar of recycled
Sites operated by government or not for profit organizations that take-back consumer goods for reuse or secondary marketing
Registered Facilities
Facilities that accept 250 tons or less per day (weekly basis) of source-separated nonputrescible recyclables based on a weekly average and have a residue rate below 15%

## Slide 31: 361-1 – Recyclables Handling and Recovery Facilities
Operating Requirements:
Only receive source-separated, nonputrescible recyclables
Recyclables must be stored in a manner which maintains recyclability
BUD material can be stored without time restriction so long as storage volumes are not exceeded
Storage or unprocessed/processed recyclables can be longer that 180 days with DEC approval

## Slide 32: Subpart 361-3
Composting and
Other Organics Recycling Facilities

## Slide 33: 361-3 – Composting and Other Organics Recycling Facilities – Exempt Facilities
On-site (no sanitary)
< 1000 lbs per week SSO
< 3000 cubic yards/yr Yard Trimmings
Animal mortalities on a farm. No more than 10 per year if not on a CAFO
Animal mortalities on property controlled by State or municipality
Animal manure and bedding
On a CAFO (no sanitary)

## Slide 34: 361-3 – Composting and Other Organics Recycling Facilities – Registered Facilities
3000 – 10,000 cubic yards/yr Yard Trimmings
5000 cubic yards of SSO per year
Animal mortalities
Digestate, if specified

## Slide 35: Subpart 361-4
Mulch Processing Facilities

## Slide 36: 361-4 – Mulch Processing Facilities – Exempt Facilities
On-site
< 10,000 cubic yards provided the pile size criteria are followed and 10 feet is maintained between piles
Storm debris from a disaster
Quarantine materials

## Slide 37: 361-4 – Mulch Processing Facilities – Registered Facilities
More than 10,000 cubic yards but less than 25,000 cubic yards, provided:
    A program is in place to keep contaminated wood out
    The facility does not accept C&D debris
    Material is processed within 12 months
    Pile sizes: Unprocessed/Rough Grind: 25’ high x 30’ wide
    Double Grind/ Long Island: 15’ high x 30’ wide
    Temperature monitoring, buffers, restacking to avoid temperatures above 140ºF, runoff controls

## Slide 38: Subpart 361-5
Construction & Demolition Debris Handling and Recovery Facilities

## Slide 39: 361-5 – C&D Debris Handling and Recovery Facilities – Registered Facilities
Facilities receiving less than 500 tons/day (weekly basis) of:
Concrete, Brick, & Rock
Asphalt Pavement or Millings
Asphalt Roofing Shingles (no asbestos)
Gypsum Wallboard
Unadulterated, Uncontaminated Wood
Uncontaminated Soil
Restricted-Use Soil/Limited-Use Soil (cannot be combined with Uncontaminated Soil)
Case-Specific BUD material derived from C&D Debris
Combination of materials above

## Slide 40: 361-1 – C&D Debris Handling and Recovery Facilities
Operating Requirements:
Throughput and Storage Volumes according to registration or permit
Management of Gypsum Wallboard, mixed C&D Debris must be in an enclosed building (Existing facilities do not need to retrofit)
Transportation from Registered and Permitted Facility requires Tracking Form - Fill material & non-BUD material
Sampling of all residue and fill material leaving facility is required

## Slide 41: Subpart 361-8
Used Cooking Oil and Yellow Grease Processing Facilities

## Slide 42: 361-8 – Used Cooking Oil and Yellow Grease Processing Facilities
Exempt Facilities:
Facilities receiving <1000 gallons per year and resultant fuel not offered for sale
Registered Facilities:
Facility receiving < 500,000 gallons
Operating Conditions:
Secondary Containment, overfill prevention, fire and building code compliance, storage time limits

## Slide 43: Part 362
Combustion, Thermal Treatment, Transfer, and Collection Facilities

## Slide 44: Part 362 Combustion, Thermal Treatment, Transfer, and Collection Facilities
Subpart 362-1 Combustion Facilities and Thermal Treatment Facilities
Subpart 362-2 Municipal Solid Waste Processing Facilities
Subpart 362-3 Transfer Facilities
Subpart 362-4 Household Hazardous Waste Collection Facilities and Events

## Slide 45: Subpart 362-1
Combustion Facilities and Thermal Treatment Facilities

## Slide 46: 362-1 – Combustion Facilities and Thermal Treatment Facilities
Exemptions:
Combustion Facility regulated under 10 NYCRR Part 70 that treats RMW on-site.
Animal Crematory regulated under 6 NYCRR 219
Facility that combusts alternative fuel authorized under 6 NYCRR Part 212 or 227

## Slide 47: 362-1 – Combustion Facilities and Thermal Treatment Facilities
Registered Facilities:
Facility that combusts/thermally treats waste tires
Facility that combusts/thermally treats unadulterated, uncontaminated wood
Facility that combusts or thermally treats used cooking oil/yellow grease
Facility that stores, prior to combustion, alternative fuel in an enclosed building/trailer/container

## Slide 48: Subpart 362-4
Household Hazardous Waste Collection Facilities and Events

## Slide 49: 362-4 – Household Hazardous Waste Collection Facilities and Events
Registered Collection Events
    No more than 24 days per calendar year
    Notify regional DEC office at least 30 days before
    Collection Event Plan
    Remove materials within 3 days
    Registration valid for one year
Permitted Collection Facility
    Satellite collection event criteria
        Collection Event Plan

## Slide 50: Part 363
Landfills

## Slide 51: 363 – Landfills – Exempt Facilities
A tree debris disposal facility (except in Nassau and Suffolk Counties) used for the disposal of tree debris provided the facility:
    Does not accept a fee or other form of consideration
    The tree debris is only accepted during daylight hours
    Tree debris is placed above the seasonal high groundwater table and not in surface water
    No more than 1 acre of the facility is used for tree debris disposal over the lifetime of the facility

## Slide 52: 363 – Landfills – Exempt Facilities
A facility (except in Nassau or Suffolk Counties) where only recognizable, uncontaminated concrete or concrete products, asphalt pavement, brick, glass, rock and general fill from construction and demolition activities, is accepted for disposal provided:
    Does not accept a fee or other form of consideration
    The waste is only accepted during daylight hours
    The waste is placed above the seasonal high groundwater table and not in surface water
    The waste does not include residues form C&D debris recovery and handling facilities
    No more than a total of 5,000 cubic yards of waste is received during the lifetime of the facility

## Slide 53: 363 – Landfills – Exempt Facilities
A facility (except in Nassau or Suffolk Counties) where waste generated by state or municipal highway projects and managed on highway rights-of-way or municipally owned properties is accepted, consisting only of recognizable, uncontaminated concrete or concrete products, asphalt pavement, brick, glass, rock and general fill, and restricted-use fill from construction and demolition activities provided:
    The waste is placed above the seasonal high groundwater table and not in surface water
    The waste does not include residues form C&D debris recovery and handling facilities

## Slide 54: 363-3 – Landfills – Inactive Disposal Facilities
Notifications for inactive disposal facilities:
The owner or operator of a disposal facility at which waste acceptance ceased prior to October 9, 1993 must notify the department in writing, of:
Any plan to disturb…
The discovery of exposed waste, surface discharge of leachate…

## Slide 55: 363-7 – Landfills – Operating Requirements
Radiation detectors required at landfills which receive MSW or authorized drilling and production wastes
Prohibition on flowback water, brine, and residues from oil/gas production
Alternative operating cover must be identified in the facility’s permit as a separate annual tonnage and be reported to the department

## Slide 56: Part 364
Waste Transporters

## Slide 57: Part 364 Waste Transporters
Subpart 364-1 General
Subpart 364-2 Exemptions
Subpart 364-3 Registrations
Subpart 364-4 Permits
Subpart 364-5 Recordkeeping and Reporting

## Slide 58: 364 – Waste Transporters – General
Applicability:
  Raw sewage, Septage, and Sludges
  Industrial-commercial waste
  Waste tires
  Waste oil
  Regulated medical waste (RMW)
  Household hazardous waste (HHW)
  Infectious waste
  Hazardous waste

## Slide 59: 364 – Waste Transporters
Exemptions include: | 
Transportation by rail, water or air | Waste transported by farm vehicles
Residential & industrial waste (exclusions apply) | C&D debris <10 cubic yards/shipment
HHW (source-separated & self transported to authorized event/facility) | Regulated waste ≤2,000 lbs/shipment (exclusions apply)
Non-hazardous bottom & fly ash | Uncontaminated drill cuttings
Public utility, railroad and transportation agency wastes (conditions apply) | Approved BUD materials
RMW <50 lbs/shipment (criteria apply) | Ag waste

## Slide 60: 364 – Waste Transporters
Registration
Required for transportation of:
    RMW <50 lbs/month (must meet specific criteria)
    HHW ≤50 lbs/shipment (source-separated)
    Sharps from a household medical waste sharps collection facility
    Commercial solid waste, other than C&D debris, >2,000 lbs/shipment
    C&D debris (includes all fill categories) >10 cubic yards/shipment
Permits
Required for everything else

## Slide 61: 364 – Waste Transporters
Reporting & Recordkeeping
Waste tracking documents required for:
      Statewide: RMW; restricted-use, limited-use & contaminated fill; and non-exempt drilling & production waste
      New York City: Statewide plus C&D debris including general fill
Annual reports due annually by March 1

## Slide 62: Part 365
Regulated Medical Waste Facilities and Other Infectious Waste

## Slide 63: Part 365 – Regulated Medical Waste and Other Infectious Wastes
Subpart 365-1 RMW Generators
Subpart 365-2 RMW Treatment, Storage, and Transfer Facilities
Subpart 365-3 Other Infectious Wastes
- Addresses incidental infectious waste that is not RMW
(e.g., Ebola, anthrax incidents)

## Slide 64: Part 366
Local Solid Waste Management Planning

## Slide 65: Part 360 Transition Requirements – LSWMPs
LSWMPs approved prior to November 4, 2017 remain in effect for term of planning period in the approved LSWMP
Draft LSWMPs submitted to the Department for review but not approved by November 4, 2017: the Department will perform a completeness review within 365 days

## Slide 66: 366 – Local Solid Waste Management Planning
Description of the planning unit
Waste generation and materials recovery data
Description of the existing solid waste management system
Description of existing administrative and financial structure
Identification of alternatives for program enhancements considered
Evaluation of the alternatives determined to be applicable
Identification of the selected alternatives and programs
Implementation plan and schedule – 10 years
Waste stream projections

## Slide 67: 366 – Local Solid Waste Management Planning
Public Participation Process
Prior to submission - 45-day public comments period
At least 1 public meeting during the public comment period
Responsiveness summary must be prepared
LSWMP Approval Process
Department review time frames added
- 30 day completeness review
- Upon completeness determination – 1 year to complete the process
- 120 days – complete draft LSWMP review
- 60 days – 2nd and subsequent submittals
- Final LSWMP approved when all documents submitted

## Slide 68: 366 – Local Solid Waste Management Planning
Subsequent LSWMP
180 days prior to expiration, a new draft LSWMP must be submitted
Optional LSWMP Planning Period Extension
Planning period can be extended two years as part of the biennial LSWMP update – maximum of 5 two-year extensions
Biennial LSWMP Update
Department can Biennial update submitted no later than May 1 every other year
LSWMP Withdrawal
determine LSWMP is no longer in effect
30 days to appeal
Right to a hearing

## Slide 69: Part 369
State Assistance Projects

## Slide 70: Part 369 – State Assistance Projects
Subpart 369-1 General Provisions
Subpart 369-2 Municipal Waste Reduction, Recycling, Household Hazardous Waste Collection and Beverage Container Assistance Capital Projects
Subpart 369-3 Municipal Waste Reduction and Recycling Education, Promotion, Planning and Coordination Projects
Subpart 369-4 Municipal Household Hazardous Waste Collection and Disposal Projects
Subpart 369-5 Targeted Priority Area Municipal Waste Reduction and Recycling Projects
Subpart 369-6 Nonhazardous Municipal Landfill Closure Projects
Subpart 369-7 Nonhazardous Municipal Landfill Gas Management Projects

## Slide 71: 369-2 – State Assistance Projects – Municipal Waste Reduction & Recycling and HHW Capital Projects
Applications reviewed in the order received and placed on a waiting list if funding is not available
Costs must be incurred no more than 1 year before the application date
Projects must be expected to last 10 years for vehicles and equipment and 30 years for structures
Projects do not include waste tires, waste oil or C&D debris
Project must be intended to serve a substantial portion of the population or handle a significant portion of the waste stream
Project must be consistent with department-approved CRA or LSWMP

## Slide 72: 369-3 – State Assistance Projects – Municipal Waste Reduction & Recycling Education, Promotion, Planning and Coordination Projects
Only one application per calendar year for all eligible costs expected to be incurred
Application must be postmarked during August, September and October for costs anticipated during the next calendar year
Project must be consistent with department-approved CRA or LSWMP
Project coordinators must be assigned to the project for no less than 50 percent of their full-time schedule for salary costs to be eligible

## Slide 73: 369-4 – State Assistance Projects – Municipal HHW Collection and Disposal Projects
Only one application per calendar year for all eligible costs incurred during the previous calendar year can be submitted
Applications must be postmarked during January and February of each calendar year for costs incurred during the previous calendar year
Costs incurred for the collection and management of materials that have an established statewide take-back, product stewardship or return program are not eligible

## Slide 74: Thank You Richard Clarkson richard.clarkson@dec.ny.gov 518-928-6709